## Slide 1
HOJUN · CLASS 12
Offshore, Worldwide
Four wind farms, four seabeds. You be the engineer.
Do English with Brian

## Slide 2
WARM-UP
Catching Up
QUESTIONS
Q1 How's the week been on site?
Q2 Anything that turned out harder than planned?
TOOLBOX
It's been ~ so far
지금까지는 ~해요
~ took longer than we planned
~가 계획보다 오래 걸렸어요
FROM YOUR WORDS · 지난주 단어
wise
universal
CAUGHT TODAY

## Slide 3
SITE 1 · UNITED KINGDOM
Hornsea 2
Ørsted · 2022 · 1.32 GW · 165 turbines at 8 MW · the world's largest when it opened
Monopiles 60–78 m long, depending on water depth · 390 km of cable · sits next to Hornsea 1 (1.2 GW)
Hornsea 3's monopiles: SeAH — a Korean company
Q1 Sixty-metre monopiles versus seventy-eight — what changes when you go longer?
↳ Length is water depth plus how deep it's driven plus height above the water. Longer means heavier, a bigger hammer, a bigger vessel, and a narrower weather window.
Q2 165 turbines, 390 km of cable. Where's the biggest risk?
↳ In the cables. Most offshore wind failures are cable faults — anchors, trawl nets, bad burial. Turbines rarely break. Cables do.
Q3 SeAH makes the monopiles for Hornsea 3. What does that tell you?
↳ Korean steel pipe is already inside the European supply chain. The next step is Korean installation and engineering — not just the steel.
TOOLBOX
· The longer the pile, the ~
· At that distance, ~
· What changes at depth is ~
· The risk moves to ~
· You'd never get away with ~
· The clever part is ~
· I'd trust ~ before ~
· If I had to bet, ~

## Slide 4
SITE 2 · UNITED KINGDOM
Dogger Bank
3.6 GW across phases A, B, C · 130–200 km offshore · water 18–63 m deep · Haliade-X 13–14 MW turbines
Monopiles up to 72.8 m long and 1,424 tons · an 8-metre flange, the largest ever · 277 monopiles in total
Chosen because it's far enough to be invisible from land, yet shallow enough for fixed foundations
Q1 130 km out. How does that change the work?
↳ A crew transfer takes hours each way, so you use service vessels that stay out for weeks. Every trip is expensive, so every mistake is expensive.
Q2 A 1,424-ton monopile with an 8-metre flange. What can go wrong on the lift?
↳ Crane capacity, swell moving the vessel, keeping the pile plumb while driving — and damaging the flange, the one part that has to be perfect for the transition piece to bolt on.
Q3 Why pick a site nobody can see?
↳ No visual complaints, stronger and steadier wind — about 10 m/s — and yet only 18 to 63 metres deep. Far away, but still standing on the seabed.
TOOLBOX
· The longer the pile, the ~
· At that distance, ~
· What changes at depth is ~
· The risk moves to ~
· You'd never get away with ~
· The clever part is ~
· I'd trust ~ before ~
· If I had to bet, ~
FROM YOUR WORDS · 지난주 단어
fade
anymore

## Slide 5
SITE 3 · NETHERLANDS
Borssele 1+2
Ørsted · 2020 · 752 MW · 94 turbines at 8 MW · 23 km off the coast of Zeeland
Monopile foundations · 94 inter-array cables, each buried two metres into the seabed
Built with jack-up vessel Innovation and cable-layer Nexus
Q1 Ninety-four cables buried two metres deep. Why bury them?
↳ Ship anchors and fishing gear are the number-one cause of cable damage. Two metres keeps them out of reach — and insurers won't cover an unburied cable.
Q2 Only 23 km from shore. What's easier, and what's harder?
↳ Easier: short cables, quick transfers, cheaper maintenance. Harder: more shipping, more fishing, more people watching, tighter permits.
Q3 94 turbines at 8 MW. Why not fewer, bigger ones?
↳ In 2020, 8 MW was the largest proven turbine. Today the same farm would use half as many 14–15 MW units — fewer foundations, fewer cables, fewer lifts.
TOOLBOX
· The longer the pile, the ~
· At that distance, ~
· What changes at depth is ~
· The risk moves to ~
· You'd never get away with ~
· The clever part is ~
· I'd trust ~ before ~
· If I had to bet, ~

## Slide 6
SITE 4 · SCOTLAND
Hywind Scotland
Equinor · 2017 · the world's first floating wind farm · 5 turbines at 6 MW · 30 MW · 29 km off Peterhead
Water 95–120 m deep · spar-buoy foundations: 90 m of steel below the surface, 3,500 tons each, held by three mooring chains
Highest capacity factor of any UK offshore wind farm (54%) · cost £264m
Q1 100-metre water. What does a monopile do there?
↳ Nothing — it can't. Fixed foundations stop making economic sense around 40 to 50 metres. Below that, you float.
Q2 A spar buoy — 90 m of steel underwater, three mooring chains, nothing in the seabed. Would you trust it?
↳ It's oil-and-gas technology; the same idea has held North Sea platforms for decades. The weight sits low, so it doesn't tip. The risk moved from the seabed to the mooring lines.
Q3 Highest capacity factor in the UK. Why would floating beat fixed?
↳ Deep water is far from shore, and far from shore means stronger, steadier wind. Floating lets you go where the wind actually is.
TOOLBOX
· The longer the pile, the ~
· At that distance, ~
· What changes at depth is ~
· The risk moves to ~
· You'd never get away with ~
· The clever part is ~
· I'd trust ~ before ~
· If I had to bet, ~
FROM YOUR WORDS · 지난주 단어
eastern
champion

## Slide 7
YOUR VERDICT
Four Seabeds, One Engineer
QUESTIONS
Q1 Of the four, which one was the hardest to build?
Q2 Which one would you want to work on?
Q3 Which one would keep you up at night?
Q4 In ten years, will most new wind farms stand on the seabed, or float?
Q5 The sea off Korea's east coast gets deep very quickly. What does that mean for wind farms there?
↳ Little shallow water on the east coast — so the big projects off Ulsan are going floating.
TOOLBOX
I'd say ~ was the hardest, because ~
제일 어려웠던 건 ~예요, 왜냐하면 ~
I'd want to be on ~
~에서 일해보고 싶어요
~ would worry me — ~
~는 걱정될 거예요 — ~
Ten years from now, ~
10년 뒤엔 ~
For Korea, that means ~
한국에선 그게 ~라는 얘기죠
CAUGHT TODAY